## Slide 1
L2 Gigabit Ethernet Switch
Network & Systems management
SNMP v1/v2, MIB II, RMON MIB, and applied to the remote network management can be more easily. CLI commands and EMS upgrade available on the system configuration and management are redefining convenience.
Improved performance
Non-blocking Switching fabric for high-performance stable and 56Gbps switching capacity and up to speed packet processing 41.6Mpps support.
Key Features
DAYOU DSW2324G
Overview
L2 Features
Port-based VLAN, IEEE 802.1q Tagged VLAN
VLAN Trunk
VLAN stacking (Q-in-Q). VLAN Translation
802.1p packet priority
Spanning Tree Protocol(STP/RSTP/MSTP)
802.3ad Link Aggregation Control Protocol
Static Trunk group
Jumbo frame 9KB
Self loop detection
Multicast
IGMP v1/v2
IGMP snooping/IGMP static join/IGMP Join Limit
Multicast Packet Filtering
QoS
Classification
L2 : SRC/DST MAC, Ether type, 802.1p priority, VLAN ID
L3 : SRC/DST IP, ToS, DSCP, IP Precedence
L4 : SRC/DST TCP/UDP port, ICMP
Mark/remark/policing
Queue scheduling (SPQ, WRR,DRR)
8 queues per port
Congestion management (RED)
Traffic policing and shaping
Rate limiting
Traffic Control
Security
MAC flood Guard/Port Flood Guard
MAC Filtering/MAC limit
Storm control (broadcast, multicast, DLF)
CPU Protection (ACL, Rate Limit)
DoS Protection
NetBIOS, NetBEUI, NBT, CIFS, SSDP, WSDD filtering
ARP/DHCP snooping , ARP Inspection
801.x Port-Based Authentication
Port isolation
Management
CLI(serial / Telnet)
Dual OS (active/backup) & Fail Over
Remote OS upgrade (FTP/ TFTP)
Multiple configuration files
Remote configuration upgrade (FTP/TFTP)
Port/Protocol mirroring
SNMP v1/v2
RMON history
Syslog
Telnet/SSH
DHCP server, relay agent with option82
DDM (Digital Diagnostics Monitoring)
LLDP (Link layer Discovery Protocol)
AAA (Authentication, Authorization, and Accounting)
NTP
TCP dump & logging
High Performance Network
DSW2324G as a high-performance network services supported by the Switch's Ethernet-based data, video, and voice services for optimal network environment.
DAYOU NETWORKS DSW2324G is L2 Gigabit Ethernet Switch as a high-end interface to support a variety of multimedia services (IPTV TPS).
Also GPON networks environment can be used in ONU for FTTH and Ethernet environment can be used in Access L2 switch. 24port Gigabit interface has been developed to fit the needs of customers who want to build a high-speed network environment as the cost of the optimal L2 switch service port to uplink. port and four(4) port of combo. Multicasting, QoS, Security, etc. Based on the outstanding performance is a system that provides a high-performance, high-quality, reliability.
DSW2324G
Security
Manager authentication protocol, RADIUS and TACACS+ only authorized users through the relevant equipment to be accessible by the system management and network management of security.

## Slide 2
Core Network
DAYOU NETWORKS SWITCH SERIES
Interface
Downlink 24port 100Base-Fx/1000Base-X(SFP)
4ports 10/100/1000BASE-T Combo
Uplink(option) 2ports 100Base-Fx/1000Base-X(SFP)
Console RS-232C(RJ-45)
Protocol
Performance
12.8Gbps Switching fabric, 9.5Mpps Throughput
16K MAC address, 4K 802.1Q VLAN
4K Active VALN
1K Multicast group entry
Memory
RAM 128Mbyte
FLASH 64Mbyte
Power
Operating Power AC88V~264/ VAC47~63Hz
Free Voltage
Power Consumption 30Watts
Operating Temperature -20℃ ~60℃(-4°F ~ 140°F)
Operating Humidity 10 ~ 90%(Non-condensing)
Ordering Information
Specifications
Dimensions
Dimension(W/H/D) 440mm x 45mm x 290mm
Weight 4.1Kg
Warranty
One-year(12month) return to factory parts
Contact Information
Website: http://www.dayounetworks.co.kr
E-mail : sales@dayounetworks.co.kr
DAYOU NETWORKS
4F, 500-2, Sangdaewon-dong, Junwon-gu,Seognam-si,
Gyeongi-do, Korea (462-120)
Tel : +82 -31 737-7125 / FAX:+82-31-737-7100
FRONT
1
2
3
5
4
6
7
REAR
1. RJ45 port of Console
2. 100/1000Base-X Ethernet Ports (1~24) ports
3. 100/1000Base-T Ethernet (1~4) ports(combo)
4. Uplink module
5. Electrical Power Input : AC Power 110 VAC ~ 220VAC Free Voltage
6. Power Switch
7. Earth Terminal